## Slide 1: CSE 577 VLSI System Design Spring 2016 Lecture 3: Design Synthesis
Vijay Narayanan
Xueqing Li
Kevin Irick
Many Thanks to Zhibo Wang and Srivatsa Rangachar

## Slide 2: Lecture Overview
Target
  Understanding the ASIC design flow using STD cells and Synopsys/Cadence tools
  Understanding design optimization trade-offs in the design synthesis
Content
  Design flow overview
  DC synthesis
  ICC layout
Lecture on Tuesday, Feb 2nd is cancelled due to ISSCC

## Slide 3: Digital Design Flow
Verilog/VHDL Design
Modelsim
Simulation
DC Synthesis
ICC Physical Design
DRC/LVS
Modelsim
Simulation
Modelsim
Simulation
Finish
This lecture
Future lectures
Previous lectures

## Slide 4: DC Synthesis
DC Synthesis
HDL design files
Technology library
Design constraints
.sdc
constraints
Verilog
Netlist
+
or .ddc file (verilog gate level descriptions and design constraints)
Input
Output

## Slide 5: DC Synthesis Step 1: Preparation
Tools
  Synopsys DC
Libraries
  Standard cell library
  IP
  I/O
  SRAM
Design files
  Verilog/VHDL files (must be synthesizable)
Design specifications
  Area, power, speed, etc.

## Slide 6: DC Synthesis Step 1: Preparation (cont.)
Synopsys environment setup: source .cshrc
Set path for design and libraries
  set project_path "/home/YourName/project/CSE577"
  set output_dir "./result”
  if {![file exists result]} { file mkdir result}
  if {![file exists "$output_dir"]} { file mkdir "$output_dir"}
  set path "$project_path/DC"
  set search_path "$path $project_path/HDLCode"
  set lib_path "/home/synopsys/lib"
  set stdlib_path "$lib_path/synopsys_dc”
  set target_library "$stdlib_path/tt_0v5.db"
  set link_library " * $stdlib_path/tt_0v5.db"
  set symbol_library "$stdlib_path/synopsys.sdb”
Set other options
  set verilogout_no_tri true
Tool command language for configurations (.tcl).
}
Projects
}
Libraries

## Slide 7: DC Synthesis Step 2: Read/Analyze the Design
Read_file command
  read_file -format vhdl {mc8051_p.vhd}
  read_file -format vhdl {addsub_core_.vhd}
  read_file -format verilog {ntcmcu.v RAM128B.v RAM1K.v}
  read_file -format verilog {ntcchip.v}
Analyze command with more check on the syntax
  analyze –work work –format verilog ntcchip.v
Link
  Will link the verilog files to libraries.

## Slide 8: DC Synthesis Step 3: Set Design Constraints
Driving, clock, delay/load, area, and other options
  set all_input_but_clock [remove_from_collection [all_inputs] {clk1 clk2}]
  set_driving_cell -lib_cell BUFX16 -pin Y $all_input_but_clock
  create_clock -period 200 [get_ports clk]
  set_clock_uncertainty -setup 0.4 [get_ports clk]
  set_clock_uncertainty -hold 3 [get_ports clk]
  set_clock_transition 0.2 [get_clocks clk]
  set_input_delay -max 2 -clock clk $all_input_but_clock
  set_input_delay -min 0 -clock clk $all_input_but_clock
  set_wire_load_model -name smic13_wl20
  set_wire_load_mode top
  set_load 0.1 [all_outputs]
  set_max_area 0
  set verilogout_show_unconnected_pins true
  set verilogout_no_tri true
  set_fix_multiple_port_nets -all -buffer_constants
  set_svf myfile.svf
Delay and load model
}
}
}
CLK
Others

## Slide 9: DC Synthesis Step 4: Compile and Generate Outputs
{
  Compile
  define_name_rules verilog -case_insensitive
  change_names -hierarchy -rules verilog
  write -h -format verilog -output "$output_dir/code_gate.v”
  write -format ddc -hierarchy -output "$output_dir/code_gate.ddc”
  write_sdc "$output_dir/code_gate.sdc"
  redirect -append -tee "$output_dir/01_Report_area.txt" {report_area -nosplit -hierarchy}
  redirect -append -tee "$output_dir/01_Report_power.txt" {report_power -hier -hier_level 100 -analysis_effort high}
  redirect -append -tee "$output_dir/01_Report_power_netcell.txt" {report_power -net -cell -analysis_effort high -sort_mode dynamic_power}
  redirect -append -tee "$output_dir/01_Report_clock.txt" {report_clock -nosplit}
  redirect -append -tee "$output_dir/01_Report_timing.txt" {report_timing -path full -delay max -nworst 1 -max_paths 3 -significant_digits 3 -sort_by group}
Gate level output
Clock & IO constraints
binary project file
Reports

## Slide 10: Digital Design Flow
Verilog/VHDL Design
Modelsim
Simulation
DC Synthesis
ICC Physical Design
DRC/LVS
Modelsim
Simulation
Modelsim
Simulation
Finish
Previous lecture
This lecture
Previous lectures

## Slide 11: ICC Layout Design Overview
PREVIOUS: Synthesis
Design Setup
Floorplanning
Place options
Clock options
Route options
Finishing
NEXT: DRC/LVS
IC Complier

## Slide 12: ICC Layout Design Step 1: Building Projects
  set source_file ./sources/code_gate.ddc
  set link_library "* $my_lib_path/smic013_dc/tt_0v5.db $my_lib_path/smic013_pad/SP013D3W_V1p1_typ.db"
  set target_library "$my_lib_path/smic013_dc/tt_0v5.db $my_lib_path/smic013_pad/SP013D3W_V1p1_typ.db"
  set symbol_library "$my_lib_path/lib/smic013_dc/smic13g.sdb”
  set timing_enable_multiple_clocks_per_reg true
  set case_anslysis_with_logic_constants true
  set physopt_delete_unloaded_cells false
  set enable_recovery_removal_arcs true
  set mw_logic0_net "VSS"
  set mw_logic1_net "VDD"

## Slide 13: ICC Layout Design Step 1: Building Projects
  create_mw_lib $my_mw_lib -open -technology $my_lib_path/tf/smic13g_8lm.tf -mw_reference_library "$my_lib_path/smic13g $my_lib_path/smic013padw $my_lib_path/LVSHIFTER ”
  set_tlu_plus_files -max_tluplus $my_lib_path/tlup/smic013_8lm_cell_max.tlup \
  -min_tluplus $my_lib_path/tlup/smic013_8lm_cell_min.tlup \
  -tech2itf_map $my_lib_path/tlup/smiclogic013_rcxt_tran.map
  check_tlu_plus_files
  import_designs ./sources/code_gate_pad.v -format verilog -top ntcchip_top
  read_sdc ./sources/code_gate_pad.sdc
  set_auto_disable_drc_nets -constant false
  remove_attribute [all_clocks] fix_hold
  check_timing
  set_zero_interconnect_delay_mode true
  redirect -tee zic.timing {report_timing}
  set_zero_interconnect_delay_mode false
  save_mw_cel -as orca_data_setup

## Slide 14: ICC Layout Design Step 2: Floor planning
Add physical only cells (CORNER), set pad locations
Pre-place macro cells and standard cells
Create pad rings
Connect power nets (done in many steps)
Pre-route power nets
Place standard cells

## Slide 15: ICC Layout Design Step 3: Clock and Routing
Set constraints (re-set)
  set_route_mode_options -zroute false
  remove_ideal_net [get_ports clk]
  read_sdc ./sources/code_gate_pad.sdc
Set clock routing rules and cells used in the clock tree
  define_routing_rule clock_rule -spacings {METAL2 0.56 METAL3 0.56 METAL4 0.56 METAL5 0.56 METAL6 0.56 METAL7 0.56}
  set_clock_tree_options -target_skew 0.1 -max_transition 0.5 -max_fanout 15 -routing_rule clock_rule -layer_list {METAL3 METAL4 METAL5}
Build clock tree and route clock nets
  reset_clock_tree_references
  set_clock_tree_references -references {CLKBUFX2 … CLKINVX20}
  clock_opt
Route all nets
  route_opt

## Slide 16: ICC Layout Design Step 4: Finishing
Finishing (07)
  Check antenna errors
  Insert standard cell fillers
  Insert metal and poly fillers
  Check DRC errors
Report Output (08)
  set_write_stream_options -map_layer $my_lib_path/gds2OutLayer.map -child_depth 20 -output_filling {fill} -output_pin {text geometry}
  write_stream -cells {ntcchip_top} ./result/ntcchip_phy.gds
  define_name_rules verilog -case_insensitive
  change_names -rules verilog -hierarchy
  remove_unconnected_ports [get_cells -hier {*}]
  write_verilog -o ./result/ntcchip_phy.v
  write_sdf ./result/ntcchip_phy.sdf

## Slide 17: References
Synopsys/Cadence user manual
Standard cell library data book
I/O library book
LAB IST218

## Slide 18: Appendix - .cshrc
#synopsys tools
setenv PATH /home/software/synopsys-2013/syn_vG-G-2012.06-SP5-2/bin:${PATH}
setenv PATH /home/software/synopsys-2013/pts-H-2012.12-SP3-1-x86/bin:${PATH}
setenv PATH /home/software/synopsys-2013/vcs-mx-vH2013.06/bin:${PATH}
setenv VCS_HOME /home/software/synopsys-2013/vcs-mx-vH2013.06
setenv PATH
/home/software/synopsys-2013/customdesigner-H-2013.03-SP2-1/bin:${PATH}
setenv PATH
/home/software/synopsys-2013/icvalidator-I-2013.12-SP2-HF1/bin:${PATH}
setenv PATH /home/software/synopsys-2013/syn_vH-2013.03-SP5-2/bin:${PATH}
setenv PATH /home/software/synopsys-2013/starrc-H-2013.06-SP2-1/bin:${PATH}
setenv PATH
/home/software/synopsys-2013/hercules-vB-2008.09-SP5-1/bin/linux:${PATH}
setenv PATH /home/software/synopsys-2013/icc-H-2013.03-SP2/bin:${PATH}
#synopsys memory compiler
setenv MC_HOME /home/software/synopsys-2013/saed_mc
setenv SAED_MC_32_28_PDK $MC_HOME/etc/techs/SAED_PDK_32/
setenv PERL5LIB $MC_HOME/lib
set path= ($path $MC_HOME/bin )
alias ise '/home/software/xilinx-13.2/ISE_DS/ISE/bin/lin64/ise'
alias matlab '/home/software/matlab_R2012b/bin/matlab’
setenv LM_LICENSE_FILE 1700@telperion.cse.psu.edu
setenv LM_LICENSE_FILE 1711@lm2.rcc.psu.edu:${LM_LICENSE_FILE}
setenv PATH
/home/software/mentorgraphics/modeltech-10.0c/modeltech/linux_x86_64:${PATH}