## Slide 1: CSE 577 VLSI System Design Spring 2016 Lecture 3: Physical Implementations
Vijay Narayanan
Xueqing Li
Kevin Irick
With Thanks to Srivatsa Rangachar, Zhibo Wang, and Moon Seok Kim

## Slide 2: Lecture Overview
Target
  Understanding the ASIC design flow using STD cells and Synopsys/Cadence/Mentor Graphics tools
  Understanding design optimization trade-offs in the design synthesis
Content
  Design flow overview
  DC synthesis
  ICC layout
  Standard Cell Libraries
Lecture on Tuesday, Feb 2nd is cancelled due to ISSCC;
Lecture/Tutorial/Demo uploaded to Angel;
Exercise: synthesize Homework 1 for lowest power/area. Due Feb 4, 2016

## Slide 3: Digital Design Flow
Verilog/VHDL Design
Modelsim
Simulation
DC Synthesis
ICC Physical Design
DRC/LVS
VCS
Simulation
VCS/PrimeTime
Simulation
Finish
This lecture
Future lectures
Previous lectures

## Slide 4: DC Synthesis
DC Synthesis
HDL design files
Technology library
Design constraints
Output Reports
Verilog
Netlist
+
Input
Output
Standard cell library, IP, I/O, SRAM
Area, power, speed, etc.

## Slide 5: DC Synthesis Step 1: Preparation
Synopsys environment setup: source .cshrc
Set path for design and libraries
  set project_path "/home/YourName/project/CSE577"
  set output_dir "./result”
  if {![file exists result]} { file mkdir result}
  if {![file exists "$output_dir"]} { file mkdir "$output_dir"}
  set path "$project_path/DC"
  set search_path "$path $project_path/HDLCode"
  set lib_path "/home/synopsys/lib"
  set stdlib_path "$lib_path/synopsys_dc”
  set target_library "$stdlib_path/tt_0v5.db"
  set link_library " * $stdlib_path/tt_0v5.db"
  set symbol_library "$stdlib_path/synopsys.sdb”
Set other options
  set verilogout_no_tri true
Tool command language for configurations (.tcl).
}
Projects
}
Libraries

## Slide 6: DC Synthesis Step 2: Read/Analyze the Design
Read_file command
  read_file -format vhdl {mc8051_p.vhd}
  read_file -format vhdl {addsub_core_.vhd}
  read_file -format verilog {ntcmcu.v RAM128B.v RAM1K.v}
  read_file -format verilog {ntcchip.v}
Analyze command with more check on the syntax
  analyze –work work –format verilog ntcchip.v
Link
  Will link the verilog files to libraries.

## Slide 7: DC Synthesis Step 3: Set Design Constraints
Driving, clock, delay/load, area, and other options
  set all_input_but_clock [remove_from_collection [all_inputs] {clk1 clk2}]
  set_driving_cell -lib_cell BUFX16 -pin Y $all_input_but_clock
  create_clock -period 200 [get_ports clk]
  set_clock_uncertainty -setup 0.4 [get_ports clk]
  set_clock_uncertainty -hold 3 [get_ports clk]
  set_clock_transition 0.2 [get_clocks clk]
  set_input_delay -max 2 -clock clk $all_input_but_clock
  set_input_delay -min 0 -clock clk $all_input_but_clock
  set_wire_load_model -name smic13_wl20
  set_wire_load_mode top
  set_load 0.1 [all_outputs]
  set_max_area 0
  set verilogout_show_unconnected_pins true
  set verilogout_no_tri true
  set_fix_multiple_port_nets -all -buffer_constants
  set_svf myfile.svf
Delay and load model
}
}
}
CLK
Others

## Slide 8: DC Synthesis Step 4: Compile and Generate Outputs
{
  Compile
  define_name_rules verilog -case_insensitive
  change_names -hierarchy -rules verilog
  write -h -format verilog -output "$output_dir/code_gate.v”
  write -format ddc -hierarchy -output "$output_dir/code_gate.ddc”
  write_sdc "$output_dir/code_gate.sdc"
  write_sdf "$output_dir/code_gate.sdf"
  redirect -append -tee "$output_dir/01_Report_area.txt" {report_area -nosplit -hierarchy}
  redirect -append -tee "$output_dir/01_Report_power.txt" {report_power -hier -hier_level 100 -analysis_effort high}
  redirect -append -tee "$output_dir/01_Report_power_netcell.txt" {report_power -net -cell -analysis_effort high -sort_mode dynamic_power}
  redirect -append -tee "$output_dir/01_Report_clock.txt" {report_clock -nosplit}
  redirect -append -tee "$output_dir/01_Report_timing.txt" {report_timing -path full -delay max -nworst 1 -max_paths 3 -significant_digits 3 -sort_by group}
Gate level netlist
Clock & IO constraints
binary project file
Reports
Timing file for Verilog simulation
Notes: *.sdc: timing constraint file for P&R
*.vg: gate-level netlist for Place & Route
*.sdf: timing file for Verilog simulation
*.ddc: binary file (i.e. all the constraints and synthesis results are recorded)
*.spf: test protocol file for ATPG tools (i.e. TetraMax)

## Slide 9: DC Synthesis Discussions
Functional verification before synthesis!
General discussions – What determines the power, speed, and area specs of your synthesized ASIC?
  Process characteristics
  Operating voltage
  Temperature
  Coding style and EDA tools
  Timing and area trade-off
  Gate, architecture, algorithm level optimizations

## Slide 10: Optimizations
Gate level
  STD cell mapping: delay, area, power
Architecture level
  Pipelining, parallelism, retiming,
  low-activity gray coding
Algorithm level
  o(N^m), o(logN)
L
H
System | 10x
RTL | 2-5x
Transistor | 0.2-2x

## Slide 11: Coding Checklist
Blocking and non-blocking assignment
Complete sensitivity list in sequential always block
Mixed clock triggering edges? Gated clock? Synchronous vs nonsynchronous?
Readable, reusable, modifiable, scalable
  Naming convention, Version control
System definition, function partition, interface specification
  Top-bottom hierarchy design
  Group working
Using n-Lint for coding style check

## Slide 12: HW1/2 - Comments
How to optimize the trade-offs
FSM minimization & Logic minimization
  States coding: binary, gray, one-hot
  Typical redundancy in HW2
Power
Speed
Area
North – South | East – West | Duration cycles
Left-turn & Red | Red | 5
Green | Red | 10
Yellow | Red | 3
Red | Left-turn & Red | 5
Red | Green | 10
Red | Yellow | 3

## Slide 13: HW1/2 – FSM Minimization
North – South | East – West | Duration cycles
Left-turn & Red | Red | 5
Green | Red | 10
Yellow | Red | 3
Red | Left-turn & Red | 5
Red | Green | 10
Red | Yellow | 3
Red | Red | 1 (Emergency)
Q: How many states are there? Minimum bits to store them?
LT & Red; Red; 0-4
Green; Red; 0-9
Yellow; Red; 0-2
Red; LT & Red; 0-4
Red; Green; 0-9
Red; Yellow; 0-2
Red; Yellow; 0
Red; Yellow; 1
Red; Yellow; 2
Em
Em
Em
Previous State
Next State
Output=(Em?)Red:Func{States}
5+10+3+5+10+3=366b

## Slide 14: HW1/2 – FSM Minimization
LT & Red; Red; 0-4
Green; Red; 0-9
Yellow; Red; 0-2
Red; LT & Red; 0-4
Red; Green; 0-9
Red; Yellow; 0-2
Red; Yellow; 0
Red; Yellow; 1
Red; Yellow; 2
Em
Em
Em
Previous State
Next State
Output=(Em?)Red:Func{States}
5+10+3+5+10+3=366b
DFF
Em
External Em
Clock
7b
Output=Func{States}

## Slide 15: HW1/2 – FSM Minimization – Moore
North – South | East – West | Duration cycles
Left-turn & Red | Red | 5
Green | Red | 10
Yellow | Red | 3
Red | Left-turn & Red | 5
Red | Green | 10
Red | Yellow | 3
Red | Red | 1 (Emergency)
LT & Red; Red; 0-4
Green; Red; 0-9
Yellow; Red; 0-2
Red; LT & Red; 0-4
Red; Green; 0-9
Red; Yellow; 0-2
Red; Yellow; 0
Red; Yellow; 1
Red; Yellow; 2
Em=1
Previous State
Next State
Output=Func{States}
Red; Red;
Red; Red;
Red; Red;
Em=0
Em=1
Em=0
Em=1
Em=0
{5+10+3+5+10+3=36}x27b

## Slide 16: Digital Design Flow
Verilog/VHDL Design
Check
DC Synthesis
ICC Physical Design
DRC/LVS
Check
Check
Finish
Previous lecture
This lecture
Previous lectures

## Slide 17: ICC Layout Design Overview
PREVIOUS: Synthesis
Design Setup
Floorplanning
Place options
Clock options
Route options
Finishing
NEXT: DRC/LVS
IC Complier

## Slide 18: IC Compiler Process
IC Compiler
DC Synthesis Output
Technology library
Design constraints
Output Reports
Verilog
Netlist
+
Input
Output
Standard cell library, IP, I/O, SRAM
Area, shape, clock, I/O, etc.
Layout GDS
+

## Slide 19: ICC Layout Design Step 1: Building Projects
Set up software tools
  Source .cshrc
Set up the libraries
Create the project
  Read the design
  Link and check correctness

## Slide 20: ICC Layout Design Step 2: Floor planning
Add physical only cells (CORNER), set pad locations
Pre-place macro cells
Preset an outline
Image from http://www.ece.umd.edu
Corner
IO PAD
Bonding/ soldering pad
ESD, Supply,
Driver, etc.
Filler
Chip Core
Memory Macro/IP

## Slide 21: IO Pads Introduction
What do they do?
What’s inside?
What types?
  Power
  Analog/RF
  Digital
  Filler
How to use?
www.armge.com
interface to core
Printed circuit board
Flip-chip substrate
die
Flip-chip substrate
Printed circuit board
Printed circuit board
Circuitry
Circuitry
VSS
VDD
PAD

## Slide 22: IO Pads Introduction
A few examples
VDD
VSS
VDD
VSS
VDD
VSS
VDD or VSS
Analog
Digital Output
Power Supply
Digital Input

## Slide 23: ICC Step 2: Floorplanning/Power
Add physical only cells (CORNER), set pad locations
Pre-place macro cells, preset chip outline
Connect power nets
Floorplanning & placement
VDD
VDD
GND
GND
Standard cells array
Standard cells array
Source:
UMBC CMPE 641 Course

## Slide 24: Floorplanning and Placement
Shared Targets
  Chip area
  Total wire length
  Critical path delay
  Routability
  Others, e.g. noise, heat, etc
Difference in block shape constraints, I/O positions, etc.
  Floorplanning: not yet fixed, soft blocks
  Placement: fixed as hard blocks
Major CAD algorithms
  Simulated Annealing
  Partition-based methods
  Heuristic algorithms, etc.

## Slide 25: ICC Layout Design Step 3: Clocking
Set constraints (re-set)
  * like in DC synthesis
Set clock routing rules and cells used in the clock tree
  define_routing_rule clock_rule -spacings {METAL2 0.56 METAL3 0.56 METAL4 0.56 METAL5 0.56 METAL6 0.56 METAL7 0.56}
  set_clock_tree_options -target_skew 0.1 -max_transition 0.5 -max_fanout 15 -routing_rule clock_rule -layer_list {METAL3 METAL4 METAL5}
Build clock tree and route clock nets
  set_clock_tree_references -references {CLKBUFX2 … CLKINVX20}
  clock_opt

## Slide 26: Major Clocking Concerns and Techniques
Concerns
  Clock skew
  Power
  Noise/jitter
  Slew rate
  Others
Techniques
  Clock distribution tree
  Buffer insertion
  Wire sizing
  Shielding
  Distance

## Slide 27: Power/Ground Grid
Main concern: current density
Example of 2-layer pg routing
Bottom level
Top layer
Top View

## Slide 28: ICC Layout Design Step 4: Route and Finishing
Route all nets
  route_opt
Routing problem is not easy…
  Given a network, find the routing tree with the minimum length
  NP-complete! Also Not all regions allows routing
Finishing
  Check antenna errors, Insert standard cell fillers, Insert metal and poly fillers, Check DRC errors, LVS
Report Output
  set_write_stream_options -map_layer $my_lib_path/gds2OutLayer.map -child_depth 20 -output_filling {fill} -output_pin {text geometry}
  write_stream -cells {ntcchip_top} ./result/ntcchip_phy.gds
  define_name_rules verilog -case_insensitive
  remove_unconnected_ports [get_cells -hier {*}]
  write_verilog -o ./result/ntcchip_phy.v
  write_sdf ./result/ntcchip_phy.sdf (timing file)
Notes: In DC:
*.sdc: timing constraint file for P&R
*.vg: gate-level netlist for Place & Route
*.sdf: timing file for Verilog simulation
*.ddc: binary file (i.e. all the constraints and synthesis results are recorded)
*.spf: test protocol file for ATPG tools (i.e. TetraMax)

## Slide 29: References and Homework
References
  Synopsys/Cadence user manual
  Standard cell library data book
  I/O library book
  Lab

## Slide 30: Homework #5
Due March 1st, 2016
Target:
  understand the icc process, go through IIC process for the traffic light system, get the output reports (timing, area, power, etc.) and physical layout (gds).
What to submit:
  A report (with snapshots in each ICC step) describing each icc step and the discussions on the icc results;
  A zip file containing: verilog design file, synthesized netlist, icc constraints and settings, icc output reports and results.
System I/O specifications (see the next slide)

## Slide 31: System specifications of the homework design
Input ports
  clock, reset, emergency; //Boolean bit
Output ports:
  LeftTurn_EW, Red_EW, Green_EW, Yellow_EW, LeftTurn_NS, Red_NS, Green_NS, Yellow_NS; //Boolean bit
  ‘0’ for a disabled light; ‘1’ for an enabled light
Functionality
  Synchronized FSM by the rising clock edge
    If emergency is sampled as ‘1’, red lights will be triggered;
    If reset is sampled as ‘1’, the system enters an initial state with the EW red traffic lights and NS green lights on (other lights off).

## Slide 32: Appendix – Standard Cell Libraries
Library Database (db file)
  Logical View (verilog description or TLF or LIB). Verilog is required for dynamic simulation. Place and route tools usually can use TLF.
  Abstract View (Cadence Abstract Generator, LEF). Information about each cell & technology information
  Physical Layout (gdsII, Virtuoso Layout Editor) or Synopsys Milkyway format, following specific design standards rules.
Timing, power and parasitics (TLF or LIB)
  Transistor and interconnect parasitics are extracted using Cadence or other extraction tools.
  Spice or Spectre netlist is generated and detailed timing simulations are performed. Power information can also be generated during these simulations.
  Data is formatted into a TLF or LIB file including process, temperature and supply voltage variations.
  Logical information for each cell is also contained in this file.

## Slide 33: Appendix - .cshrc
#synopsys tools
setenv PATH /home/software/synopsys-2013/syn_vG-G-2012.06-SP5-2/bin:${PATH}
setenv PATH /home/software/synopsys-2013/pts-H-2012.12-SP3-1-x86/bin:${PATH}
setenv PATH /home/software/synopsys-2013/vcs-mx-vH2013.06/bin:${PATH}
setenv VCS_HOME /home/software/synopsys-2013/vcs-mx-vH2013.06
setenv PATH
/home/software/synopsys-2013/customdesigner-H-2013.03-SP2-1/bin:${PATH}
setenv PATH
/home/software/synopsys-2013/icvalidator-I-2013.12-SP2-HF1/bin:${PATH}
setenv PATH /home/software/synopsys-2013/syn_vH-2013.03-SP5-2/bin:${PATH}
setenv PATH /home/software/synopsys-2013/starrc-H-2013.06-SP2-1/bin:${PATH}
setenv PATH
/home/software/synopsys-2013/hercules-vB-2008.09-SP5-1/bin/linux:${PATH}
setenv PATH /home/software/synopsys-2013/icc-H-2013.03-SP2/bin:${PATH}
#synopsys memory compiler
setenv MC_HOME /home/software/synopsys-2013/saed_mc
setenv SAED_MC_32_28_PDK $MC_HOME/etc/techs/SAED_PDK_32/
setenv PERL5LIB $MC_HOME/lib
set path= ($path $MC_HOME/bin )
alias ise '/home/software/xilinx-13.2/ISE_DS/ISE/bin/lin64/ise'
alias matlab '/home/software/matlab_R2012b/bin/matlab’
setenv LM_LICENSE_FILE 1700@telperion.cse.psu.edu
setenv LM_LICENSE_FILE 1711@lm2.rcc.psu.edu:${LM_LICENSE_FILE}
setenv PATH
/home/software/mentorgraphics/modeltech-10.0c/modeltech/linux_x86_64:${PATH}