## Slide 1: CSE 577 VLSI System Design Spring 2016 Lecture 1: Introduction
Vijay Narayanan
Xueqing Li
Kevin Irick

## Slide 2: Course Administration
Instructors: Vijay Narayanan vijay@cse.psu.edu Xueqing Li
Guest Instructor: Dr. Kevin Irick
Labs: IST 218/220
Text/Slides: Check for reading material in Angel
Notes: computer accounts are automatic, if have never had an account in CSE I will have (or soon have) a listing of userids/passwords.
seating chart – assignment for Thursday – xerox copy of your photo ID
pick a seat for the semester and sit there (or nearby) for rest of semester
room size -

## Slide 3: Course Contents
Introduction to ASIC/FPGA Design Flow
System Design Project
Course goals
  Ability to design and implement digital circuits using standard cell design flow
  Prototype and functionally emulate the chip functionality using modern FPGA architectures using synthesizable HDL and exploiting various features of state-of-the-art FPGA design flow

## Slide 4: Grading Information
Grade determinates
  Homeworks/Lab Assignments ~40%
  Course Projects ~ 50%
  Class Participation/Individual Assessments ~10%
Many of the projects/homework may require group effort. The Individual assessment will be designed to check individual contributions.
Notes: Note: evening midterm exam
Design intensive class – with semester design project

## Slide 5: Course Structure
Design and tool intensive class
  Xilinx ISE and EDK and IBM CAPI
    Online documentation and tutorials
  Cadence/Mentor Graphics ASIC Design Flow
Lectures:
  First 8 weeks mostly to get you upto to pace with design flow
  Once Project starts, we will get to more theoretical underpinnings.
Notes: if you have never used a Unix system - you have that to learn as well!

## Slide 6: Design Options

## Slide 7: Design Spectrum
Source: RUSSELL TESSIER AND WAYNE BURLESON
Reconfigurable Computing for Digital Signal Processing: A Survey, JVLSISP, 2001

## Slide 8: Chip Fabrication

## Slide 9: Design Alternatives
Decreasing performance; Increasing flexibility
  ASIC – Application Specific Integrated Circuits
    Custom Design
    Cell Based Design
  Mask Programmable Gate Arrays
  Structured ASICs
  FPGA/FPLD
  ASIC type Custom mask layers Custom logic cells
  Full-custom All Some
  Semicustom/Cell-based All None
  MPGA Some None
  Structured ASIC Some None
  FPGA None None
Further Reading: Online Textbook ASICs by Smith - Chapter 1

## Slide 10: Custom ASIC

## Slide 11: Disadvantage of ASICs

## Slide 12: Standard Cell ASICs

## Slide 13: Standard Cell Design

## Slide 14: Standard Cell ASIC
All mask layers are customized: transistors and interconnect
Fabrication is still costly and slow

## Slide 15: Programmable Logic Devices
Standard ICs, available in standard configurations, sold in high volume
No customized cells or masks, just a single large block of programmable interconnect
Can be configured/programmed to create a specialized device

## Slide 16: System on Chip

## Slide 17: FPGAs
ZYNQ 7000

## Slide 18: New System on Chips
The integration of (nearly) all necessary electronic functions of a
system in one package
Characterized by high bandwidth and low latency integration of
– Programmable processors
– Accelerator units
– Memories
– IO functions
Software programmable

## Slide 19: FPGA vs ASIC Design Flow

## Slide 20: FPGA vs ASIC

## Slide 21: ASIC Design FLow

## Slide 22: RTL Synthesis FLow

## Slide 23: FPGA Toolflow
Source: Xilinx

## Slide 24: From Verilog to Bitstream

## Slide 25: Design Synthesis
Interpret RTL code and translate it to produce synthesized circuit netlist in a standard EDIF format
Some can display circuit schematics corresponding to EDIF netlist
module d_register (CLK, DATA, Q);
input CLK;
input DATA;
output Q;
reg Q;
always @ (posedge CLK)
begin: My_D_Reg
Q <= DATA;
end
endmodule
D
Reg

## Slide 26: Circuit netlist

## Slide 27: Technology Mapping
LUT2
LUT3
LUT4
LUT5
LUT1
FF1
FF2
LUT0
Process of binding technology-dependent circuits of target technology to
technology-independent circuits

## Slide 28: Mapping a Design into LUTs

## Slide 29: Clustering LUTs into a CLB/LAB
Clustering groups LUTs into CLB-sized clusters
- Connecting LUTs within a CLB is cheap (speed/power/area)

## Slide 30: Placement
Finding physical locations in the FPGA to implement the Clustered logic.

## Slide 31: Placement
CLB SLICES
FPGA

## Slide 32: Routing
Programmable Connections
FPGA
Connecting the clusters

## Slide 33: Static Timing Analyzer
Performs static analysis of the circuit performance
Reports critical paths with all sources of delays
Determines maximum clock frequency

## Slide 34: Static Timing Analysis
Critical Path – The Longest Path From Outputs of Registers to Inputs of Registers
D
Q
in
clk
D
Q
out
tP logic
tCritical = tP FF + tP logic + tS FF

## Slide 35: Configuration
Once a design is implemented, you must create a file that the FPGA can understand
  This file is called a bit stream: a BIT file (.bit extension)
The BIT file can be downloaded directly to the FPGA, or can be converted into a PROM file which stores the programming information

## Slide 36: Timing Metrics
clock
In
Out
data
stable
output
stable
output
stable
time
time
time
clock
D
Q
In
Out
tsu
thold
tc-q
Notes: tsetup – time that the data inputs (D) must be valid before the clock transition (0 ti 1 transition for a positive edge-triggered device)
thold is the time that the data inputs must remain valid after the clock edge
Tc-q is the worst case propagation delay (with reference to the clock edge) – time to copy D to Q

## Slide 37
Figure 5.14. Timing for a flip-flop.

## Slide 38: How fast can a circuit operate?
C
D
Q
Q'
C
D
Q
Q'
C
D
Q
Q'
C
D
Q
Q'
C
D
Q
Q'
C
D
Q
Q'
C
D
Q
Q'
C
D
Q
Q'
C
D
Q
Q'
C
D
Q
Q'
CLOCK
CLOCK

## Slide 39: Circuit and System Level Timing
If the clock period is too short, some data changes will not propagate through the circuit to flip-flop inputs before the setup time interval begins
C
D
Q
Q'
C
D
Q
Q'
C
D
Q
Q'
C
D
Q
Q'
C
D
Q
Q'
C
D
Q
Q'
C
D
Q
Q'
C
D
Q
Q'
C
D
Q
Q'
C
D
Q
Q'
CLOCK
CLOCK

## Slide 40: Circuit and System Level Timing (continued)
New Timing Components
  tp - clock period - The interval between occurrences of a specific clock edge in a periodic clock
  tpd,COMB – longest total delay of combinational logic along the path from flip-flop output to flip-flop input
  tslack - extra time in the clock period in addition to the sum of the delays and setup time on a path
    Can be either positive or negative
    Must be greater than or equal to zero on all paths for correct operation

## Slide 41: Circuit and System Level Timing (continued)
Timing Equations tp = tslack + (tcQ,FF + tpd,COMB + ts)
  For tslack greater than or equal to zero, tp ≥ max (tcQ,FF + tpd,COMB + ts) for all paths from flip-flop output to flip-flop input

## Slide 42: How fast can you clock this?
Consider a FF with following characteristics
Setup time = 0.6ns
Hold time = 0.4ns
TcQ = (0.8ns to 1.0ns) -- range not a single value
Delay of transistors vary with temperature, sizing etc.
tpd,inv = 1.1 ns (1 + 0.1k) where K is the number of gate inputs

## Slide 43: How fast can you clock this?
Consider a FF with following characteristics
Setup time = 0.6ns
Hold time = 0.4ns
TcQ = (0.8ns to 1.0ns) -- range not a single value
Delay of transistors vary with temperature, sizing etc.
tpd,inv = 1.1 ns (1 + 0.1k) where K is the number of gate inputs
1.0 (delay of flip flop) + 1.1 (inverter) + 0.6 (set-up time) = 2.7ns
1/2.7 = 370.37 MHz

## Slide 44: Short paths and hold time
Consider a FF with following characteristics
Setup time = 0.6ns
Hold time = 0.4ns
TcQ = (0.8ns to 1.0ns) -- range not a single value
Delay of transistors vary with temperature, sizing etc.
tpd,inv = 1.1 ns (1 + 0.1k) where K is the number of gate inputs
Shortest path back to input is 0.8 + 1.1 = 1.9ns > hold time

## Slide 45: Short paths and hold time
Consider a FF with following characteristics
Setup time = 0.6ns
Hold time = 0.4ns
TcQ = (0.8ns to 1.0ns) -- range not a single value
Delay of transistors vary with temperature, sizing etc.
tpd,inv = 1.1 ns (1 + 0.1k) where K is the number of gate inputs
Shortest path back to input is 0.8 + 1.1 = 1.9ns > hold time

## Slide 46: How fast can you clock this?
Longest path between flip-flop to
flip-flop
tpd,comb = 3 And gates + 1 XOR
= 3 (1 +.1*2) + 1 (1 + .1*2)
(remember 1+ .1*K assumption)
Tp = 1.0 (TcQ max) + tpd,comb + 0.6 (tsu)
= 6.4ns
Max frequency = 1/6.4ns
= 156.25 MHz

## Slide 47: Short paths and hold time
shortest path between flip-flop to
flip-flop
tpd,comb-shortest = 1 xor
= 1 (1 + .1*2)
(remember 1+ .1*K assumption)
Tp,shortest = 0.8 (TcQ min) + tpd,comb
= 2.0ns
< thold = 0.4ns

## Slide 48: Redesigned faster circuit ?
Tp = 1.0 (TcQ max) + tpd,comb + 0.6 (tsu)
= 1 + 1.2 * 4 + 0.6 = 6.4ns
Max frequency = 1/6.4ns
= 156.25 MHz
Tp = 1.0 (TcQ max) + tpd,comb + 0.6 (tsu)
= 1 + 1.4 + 1.2 + 0.6 = 4.2ns
Max frequency = 1/4.2
= 238.1 MHz

## Slide 49: Synchronous Timing Basics
Under ideal conditions (i.e., when tclk1 = tclk2)
T  tc-q + tplogic + tsu
thold ≤ tc-q, shortest +tplogic, shortest
Under real conditions, the clock signal can have both spatial (clock skew) and temporal (clock jitter) variations
  skew is constant from cycle to cycle (by definition); skew can be positive (clock and data flowing in the same direction) or negative (clock and data flowing in opposite directions)
  jitter causes T to change on a cycle-by-cycle basis
D
Q
R1
Combinational
logic
D
Q
R2
clk
In
tclk1
tclk2
tc-q, tsu,thold
tplogic, tcdlogic (tplogic, shortest)
Notes: Skew delta is tphi’’ – tphi’ where tphi’s are the local clock times. Skew can be positive or negative depending on the routing direction of the clock.
tmin’s are the best case delays of the logic, tmax are the worst case delays (assume register set up time is included in the combinational logic time). ti is the propagation delay of the interconnect.
Clock skew is due to spatial variations in the arrival time of a clock transition
  skew is constant from cycle to cycle (by definition)
  can be positive (clock and data flowing in the same direction) or negative (clock and data flowing in the opposite direction)
Clock jitter is due to temporal variations in the clock period (T changes on a cycle-by-cycle basis)

## Slide 50: Sources of Clock Skew and Jitter in Clock Network
PLL
1
2
4
3
5
6
7
clock generation
clock drivers
power supply
interconnect
capacitive load
capacitive coupling
temperature
Skew
  manufacturing device variations in clock drivers
  interconnect variations
  environmental variations (power supply and temperature)
Jitter
  clock generation
  capacitive loading and coupling
  environmental variations (power supply and temperature)
Notes: clock is distributed using multiple matched paths to the sequential elements. The clock path includes the wiring and the associated distributed buffers required to drive the interconnect and loads.
What matters is the relative arrival time at the register points at the end of each path – not the absolute delay through the clock distribution path.
Both systematic (nominally identical from chip to chip and predictable – so easy to model and correct for at design time) and random (due to manufacturing variations – so are difficult to model and eliminate)

## Slide 51: Positive Clock Skew
D
Q
R1
Combinational
logic
D
Q
R2
clk
In
tclk1
tclk2
delay
T
T + 
 > 0
 + thold
T :
thold :
1
2
3
4
Clock and data flow in the same direction
Notes: For class handout

## Slide 52: Positive Clock Skew
D
Q
R1
Combinational
logic
D
Q
R2
clk
In
tclk1
tclk2
delay
 > 0: Improves performance, but makes thold harder to meet. If thold is not met (race conditions), the circuit malfunctions independent of the clock period!
T
T + 
 > 0
 + thold
T +   tc-q + tplogic + tsu so T  tc-q + tplogic + tsu - 
thold +  ≤ tcdlogic + tcdreg so thold ≤ tcdlogic + tcdreg - 
1
2
3
4
Clock and data flow in the same direction
T :
thold :
Notes: For lecture
clock skew has the potential to improve the performance of the circuit.
Unfortunately, increasing skew makes the circuit more susceptible to race conditions! If the minimum delay of the combinational logic block is small, the inputs to R2 may change before R2’s first rising edge. To avoid races, we must ensure that the minimum delay through the register and logic must e long enough that the inputs to R2 are valid for a hold time after that edge. Reducing the clock frequency can’t fix it!

## Slide 53: Negative Clock Skew
D
Q
R1
Combinational
logic
D
Q
R2
clk
In
tclk1
tclk2
delay
Clock and data flow in opposite directions
T
T + 
 < 0
1
2
3
4
T :
thold :
Notes: For class handout

## Slide 54: Negative Clock Skew
D
Q
R1
Combinational
logic
D
Q
R2
clk
In
tclk1
tclk2
delay
Clock and data flow in opposite directions
T
T + 
 < 0
T +   tc-q + tplogic + tsu so T  tc-q + tplogic + tsu - 
thold +  ≤ tcdlogic + tcdreg so thold ≤ tcdlogic + tcdreg - 
1
2
3
4
 < 0: Degrades performance, but thold is easier to meet (eliminating race conditions)
T :
thold :
Notes: For lecture
a negative skew adversely impacts the performance of the system.
However, assuming thold + delta < tcdreg + tcdlogic, a negative skew implies that the system never fails since edge 2 happens before edge 1 – i.e., there is never a race condition.
Unfortunately, for general logic signals flow in both directions so skew can be both positive and negative in the same circuit

## Slide 55: Clock Jitter
Jitter causes T to vary on a cycle-by-cycle basis
R1
Combinational
logic
clk
In
tclk
T
-tjitter
+tjitter
T - 2tjitter  tc-q + tplogic + tsu so T  tc-q + tplogic + tsu + 2tjitter
Jitter directly reduces the performance of a sequential circuit
T :
Notes: for lecture

## Slide 56: Combined Impact of Skew and Jitter
D
Q
R1
Combinational
logic
D
Q
R2
In
tclk1
tclk2
Constraints on the minimum clock period ( > 0)
 > 0 with jitter: Degrades performance, and makes thold even harder to meet. (The acceptable skew is reduced by jitter.)
T
T + 
 > 0
1
6
12
-tjitter
T  tc-q + tplogic + tsu -  + 2tjitter thold ≤ tcdlogic + tcdreg –  – 2tjitter

## Slide 57: Repeat with Clock Skew (1.5ns)
Longest path between flip-flop to
flip-flop (clock at FF3 arrives later
1.5ns than at FF0-FF2
tpd,comb = 3 And gates + 1 XOR - skew
= 3 (1 +.1*2) + 1 (1 + .1*2) – 1.5
(remember 1+ .1*K assumption)
Tp = 1.0 (TcQ max) + tpd,comb + 0.6 (tsu)
= 4.9ns
Max frequency = 1/4.9ns = 204 MHz
Note: Can Change critical path
FF0
FF1
FF2
FF3
CLOCK
1.5ns

## Slide 58: Repeat with Clock Skew (1.5ns)
Longest path between flip-flop to
flip-flop (clock at Q3 arrives later
0.6ns than at Q1
Tp = 1.0 (TcQ max) + 3.6 + 0.6 (tsu)
= 5.2ns
Q0 to Q2 delay is 5.2ns
Q0 to Q3 was
FF0
FF1
FF2
FF3
CLOCK
1.5ns

## Slide 59: Repeat with Clock Skew (1.5ns)
Q0 to Q2 delay is 5.2ns (with no
skew between Q0 and Q2)
Hold time for shortest path that start
Elsewhere and end at Q3
0.8 + 1.2 + 1.2 = 3.2 ns
< thold (0.4) + t skew (1.5)
If skew becomes greater than 2.8 ..
We will have hold problem.
FF0
FF1
FF2
FF3
CLOCK
1.5ns

## Slide 60: Xilinx Design Flow

## Slide 62: Design Entry and Synthesis

## Slide 63: Design Implementation
Translate: The Translate process merges all of the input netlists and design constraints and outputs a Xilinx native generic database (NGD) file, which describes the logical design reduced to Xilinx primitives. (NGDBUILD)
Map: The Map process maps the logic defined by an NGD file into FPGA elements, such as CLBs and IOBs. The output design is a native circuit description (NCD) file that physically represents the design mapped to the components in the Xilinx FPGA. (MAP)
Place and Route: The Place and Route process takes a mapped NCD file, places and routes the design, and produces an NCD file that is used as input for bitstream generation. (PAR)
Programming File Generation: The Generate Programming File process produces a bitstream for Xilinx device configuration. After the design is completely routed, you must configure the device so it can execute the desired function. (Bitgen)

## Slide 64: Design Implementation

## Slide 65: Design Verification

## Slide 66: Design Verification Tools
TRACE: Timing Reporter and Circuit Evaluator
Chipscope: inbuilt logic Analyzer