## Slide 1: CSE 577 VLSI Systems Design Spring 2016
Vijaykrishnan (Vijay) Narayanan (cse.psu.edu/~vijay)
Xueqing Li and Kevin Irick
Course material on ANGEL: cms.psu.edu
Verilog Examples
Includes material from: - Brown, et al. Fundamentals of Digital Logic with Verilog Design

## Slide 2: Hardware Description Language
Examples: VHDL and Verilog
  C-like syntax
  Amenable to software engineering techniques
Programming language to describe hardware
  Assumed concurrency vs. assumed serialization
  Explicit spatial parallelism, resource utilization
  Timing dependent behavior
  Need to describe HW, its interactions with the outside world, and the testing/verification of HW all in one language!
    On the one hand, HDLs are rich languages
    On the other hand, NOT ALL HDL CODE DESCRIBES ACTUAL HARDWARE!
(See Appendix A)

## Slide 3: The Verilog language
Verilog is a case sensitive language (with a few exceptions)
Identifiers (space-free sequence of symbols)
  upper and lower case letters from the alphabet
  digits (0, 1, ..., 9)
  underscore ( _ )
  $ symbol (only for system tasks and functions)
  Max length of 1024 symbols
Terminate lines with semicolon
Single line comments: // A single-line comment goes here
Multi-line comments: /* Do not /* nest multi-line comments*/ like this */

## Slide 4: Verilog Datatype Categories
type [range] signal_name1{, signal_name2, … signal_n};
Types
  Net
    Represents a physical wire
    Describes structural connectivity
    wire and tri (tristate) keywords
    wire x; // scalar net x – 1 four-valued bit {0, 1, z, x}
    wire Cin, AddSub; // 2 scalar nets
    wire [3:0] S; // 4-bit (bus/vector) value can use S[3] to refer to 4th bit
  Variables
    Used to describe behavior or logic function
    reg and integer keywords
    reg [2:0] count; // can be sequential or combinational
    Integer k; // does not correspond directly to circuit element

## Slide 5: Arrays
reg [7:0] R[3:0];
  R as four 8-bit variables assigned as R[3], R[2], R[1] and R[0]
  Can also access them as R[3][7];

## Slide 6: Hardware Description Language - Verilog
Programming Language to describe hardware
  // Anything that starts with this is a comment
  // SPACE, TAB are ignored by Verilog Compiler
  // Verilog signals can take 0, 1, z (tri-state) or x (unknown)
  // z or Z are equivalent
  // [size][‘radix]constant 3’b001 3 bits long Binary 001
  // 2’d21 2 digit long decimal number 21
  // h – hex and o – octal
  // 8’b0000_1111 _ is only for readability and permitted
  wire [3:0] S;
  S = 4’b0011; // S[3]=0; S[2]=0; S[1]=1; S[0]=1;
Notes: Add examples from page 15 – ciletti

## Slide 7: Primitives
Common combinational logic gates
  and, nand, or, nor, xor, xnor, buf, not
  or(x,a,b,c); // instance name is optional
  or name_it_my_or(x,a,b,c) // or(output,in1,in2,in3)
Appendix A.9

## Slide 8: Primitives
and name_it_my_and(x,a,b,c);

## Slide 9: Bigger Circuit

## Slide 10: Verilog Operators
Arithmetic
  +, -, *, /, **, %
Logical
  !, &&, ||, >, >=, <, <=, ==, ===, !=, !==
Bitwise
  ~, &, |, ^, ~^
Replicate/Concatenate
  {a,b,c}
  {3{a}}
  {{5{a}},b}
Shift
  <<, <<<, >>, >>>
Unary Reduction
  &, ~&, |, ~|, ^, ~^

## Slide 11: Bitwise Operations
~ negation; // example ~1000 = 0001
& And; // example 1010 & 1000 = 1000
^ Exclusive or; // example 1010 ^ 1000 = 0010
| inclusive or; // example 1010 | 1000 = 1010
~^ exclusive nor // example 1010 ~^ 1000 = 1101
y[2:0] = a[2:0] | b[2:0];
/* is equivalent to
or(y[2],a[2],b[2]);
or(y[1],a[1],b[1]);
or(y[0],a[0],b[0]);
*/

## Slide 12: Table A.1 from Brown and Vranesic
Category | Examples | Bit Length [L = length function]
Bitwise | ~A, +A, -A A&B, A¦B, A~^B, A^B | L(A) Max(L(A),L(B))
Logical | !A, A&&B, A¦¦B | 1 bit
Reduction | &A, ~&A, ¦A, ~¦A, ^~A, ^A | 1 bit
Relational | A==B, A!=B, A>B, A<B, A>=B, A<=B, A===B, A!==B | 1 bit
Arithmetic | A+B, A-B, A*B, A/B, A%B | Max(L(A), L(B))
Shift | A<<B, A >>B | L(A)
Concatenate | {A,…,B} | L(A)+…+L(B)
Replication | {B{A}} | B*L(A)
Condition | A?B:C | Max(L(B),L(C))

## Slide 13: Logical operations
Used for taking Boolean expression and returns True or False
! – negation
&& - logical and
|| - logical or
A===B // A identical to B including x and z
A == B // not including x and z

## Slide 14: Logical Shift Operation
A = 8’b1010_0001;
A >> 1; // logical shift right
// A becomes 0101_0000;
A = 8’b1010_0001;
A << 1; // logical shift left
// A becomes 0100_0010;

## Slide 15: Arithmetic Shift Operation (will revisit again)
A = 8’b1010_0001;
A >>> 1; // arithmetic shift right
// A becomes 1101_0000; //NOTE: leftmost bit retained
A = 8’b1010_0001;
A <<<1; // arithmetic shift left (same effect as logical)
// A becomes 0100_0010;

## Slide 16: Modular Design
module
module
name [(port
name{,
port
name})];
[parameter
declarations]
[input
declarations]
[output
declarations]
[inout
declarations]
[wire
or
tri
declarations]
[reg
or
integer
declarations]
[function
or
task
declarations]
[assign
continuous assignmen
ts]
[initial
block]
[always
blocks]
[gate instantiations]
[module
instantiations]
endmo
dule
Appendix A in textbook

## Slide 17: Modules
The module is the basic building block in Verilog
Modules can be interconnected to describe the structure of your digital system
Modules start with keyword module and end with keyword endmodule

## Slide 18: Modeling Structure: Modules
  The module is the basic building block in Verilog
  Modules can be interconnected to describe the structure of your digital system
  Modules start with keyword module and end with keyword endmodule

## Slide 19: Modeling Structure: Ports
Module Ports
  Similar to pins on a chip
  Provide a way to communicate with outside world
  Ports can be input, output or inout

## Slide 20: Modeling Structure: instances
Module instances
  Verilog models consist of a hierarchy of module instances

## Slide 21: How to Build and Test a Module
Construct a “test bench” for your design
  Develop your hierarchical system within a module that has input and output ports (called “design” here)
  Develop a separate module to generate tests for the module (“test”)
  Connect these together within another module (“testbench”)
module design (a, b, c);
input a, b;
output c;
…
module test (q, r);
output q, r;
initial begin
//drive the outputs with signals
…
module testbench ();
wire l, m, n;
design d (l, m, n);
test t (l, m);
initial begin
//monitor and display
…
Adapted from Slides of Prof. Don Thomas, CMU

## Slide 22: Another View of This
3 chunks of Verilog, one for each of:
Your hardware
called
DESIGN
TESTBENCH is the final piece of hardware which
connects DESIGN with TEST so the inputs generated
go to the thing you want to test...
Another module, called TEST, to generate interesting inputs
Adapted from Slides of Prof. Don Thomas, CMU

## Slide 23: An Example
Module testAdd generated inputs for module halfAdd and displayed changes. Module halfAdd was the design
module tBench;
wire su, co, a, b;
halfAdd ad (su, co, a, b);
testAdd tb (a, b, su, co);
endmodule
module halfAdd (sum, cOut, a, b); output sum, cOut;
input a, b;
xor #2 (sum, a, b);
and #2 (cOut, a, b);
endmodule
module testAdd (a, b, sum, cOut);
input sum, cOut;
output a, b;
reg a, b;
initial begin
$monitor ($time,,
“a=%b, b=%b, sum=%b, cOut=%b”,
a, b, sum, cOut);
a = 0; b = 0;
#10 b = 1;
#10 a = 1;
#10 b = 0;
#10 $finish;
end
endmodule
Adapted from Slides of Prof. Don Thomas, CMU

## Slide 24: The Test Module
$monitor
  prints its string when executed.
  after that, the string is printed when one of the listed values changes.
  only one monitor can be active at any time
  prints at end of current simulation time
Function of this tester
  at time zero, print values and set a=b=0
  after 10 time units, set b=1
  after another 10, set a=1
  after another 10 set b=0
  then another 10 and finish
module testAdd(a, b, sum, cOut);
input sum, cOut;
output a, b;
reg a, b;
initial begin
$monitor ($time,,
“a=%b, b=%b, sum=%b,
cOut=%b”,
a, b, sum, cOut);
a = 0; b = 0;
#10 b = 1;
#10 a = 1;
#10 b = 0;
#10 $finish;
end
endmodule
Adapted from Slides of Prof. Don Thomas, CMU

## Slide 25: Another Version of a Test Module
Multi-bit “thingies”
  test is a two-bit register and output
  It acts as a two-bit number (counts 00-01-10-11-00…)
  Module tBench needs to connect it correctly — mod halfAdd has 1-bit ports.
module testAdd (test, sum, cOut);
input sum, cOut;
output [1:0] test;
reg [1:0] test;
initial begin
$monitor ($time,,
"test=%b, sum=%b, cOut=%b",
test, sum, cOut);
test = 0;
#10 test = test + 1;
#10 test = test + 1;
#10 test = test + 1;
#10 $finish;
end
endmodule
module tBench;
wire su, co;
wire [1:0] t;
halfAdd ad (su, co, t[1], t[0]);
testAdd tb (t, su, co);
endmodule
Connects bit 0 or wire t to this port (b of the module halfAdder)
Adapted from Slides of Prof. Don Thomas, CMU

## Slide 26: Another Version of testAdd
Other procedural statements
  You can use “for”, “while”, “if-then-else” and others here.
  This makes it easier to write if you have lots of input bits.
module tBench;
wire su, co;
wire [1:0] t;
halfAdd ad (su, co, t[1], t[0]);
testAdd tb (t, su, co);
endmodule
module testAdd (test, sum, cOut);
input sum, cOut;
output [1:0] test;
reg [1:0] test;
initial begin
$monitor ($time,,
"test=%b, sum=%b, cOut=%b",
test, sum, cOut);
for (test = 0; test < 3; test = test + 1)
#10;
#10 $finish;
end
endmodule
Adapted from Slides of Prof. Don Thomas, CMU

## Slide 27: Modules

## Slide 28: Example logic circuit – Hardware Description

## Slide 29: Example logic circuit – Hardware Description
module example2 (x1, x2, x3, x4, f, g, h);
input x1, x2, x3, x4;
output f, g, h;
and (z1, x1, x3);
and (z2, x2, x4);
or (g, z1, z2);
or (z3, x1, ~x3);
or (z4, ~x2, x4);
and (h, z3, z4);
or (f, g, h);
endmodule

## Slide 30: Module Ports
What and why of ports
  Similar to pins on a chip
  Provide a way to communication with outside world
  Ports can be input, output, or inout
    inout used to describe bidirectional pins
    Mostly only used at highest level of design hierarchy
  It is not necessary for a module to have ports
    Common when describing a testbench

## Slide 31: Ports
module circuit
(
//Input Port Definitions
input a,
input b,
input c,
input s,
//Output Port Definitions
output x,
output y,
output z,
//Inout Port Definitions
inout h
);
//Module Body
assign x = a | b | c;
assign y = a & b & c & h;
assign z = ~(a & b & c & h);
assign h = (s == 1'b1) ? x : 1'bz;
endmodule

## Slide 32: Instantiation
Module Instances
  Verilog models consist of a hierarchy of module instances
  These instances are interconnected using nets
    Verilog “wires”
  Think “wiring up a circuit board”
    instances are specific components
    We use wires to interconnect the components

## Slide 33: Instantiation
module circuit
(
//Input Port Definitions
input a,
input b,
input c,
//Output Port Definitions
output x
);
//Declare a net
wire temp;
//Instantiate a 2-Input AND Gate and call it A0
AND2 A0
(
.i0 (a ),
.i1 (b ),
.o (temp )
);
//Instantiate a 2-Input AND Gate and call it A1
AND2 A1
(
.i0 (temp ),
.i1 (c ),
.o (x )
);
endmodule
module AND2
(
//Input Port Definitions
input i0,
input i1,
//Output Port Definitions
output o
);
assign o = i0 & i1;
endmodule

## Slide 34: Instantiation
module circuit
(
//Input Port Definitions
input a,
input b,
input c,
//Output Port Definitions
output x
);
//Declare a net
wire temp;
//Instantiate a 2-Input AND Gate and call it A0
AND2 A0
(
.i0 (a ),
.i1 (b ),
.o (temp )
);
//Instantiate a 2-Input AND Gate and call it A1
AND2 A1
(
.i0 (temp ),
.i1 (c ),
.o (x )
);
endmodule
module AND2
(
//Input Port Definitions
input i0,
input i1,
//Output Port Definitions
output o
);
assign o = i0 & i1;
endmodule
Instance Name is “A0”
Instance Type is “AND2”
Port belonging to “this” module
Port belonging to “AND2” module

## Slide 35: Modular Design

## Slide 36: Structural Vs. Behavioral Models
Structural model
  Just specifies primitive gates and wires
  i.e., the structure of a logical netlist
  You basically know how to do this now.
Behavioral model
  More like a procedure in a programming language
  Still specify a module in Verilog with inputs and outputs...
  ...but inside the module you write code to tell what you want to have happen, NOT what gates to connect to make it happen
  i.e., you specify the behavior you want, not the structure to do it
Why use behavioral models
  For testbench modules to test structural designs
  For high-level specs to drive logic synthesis tools

## Slide 37: Structural vs. Behavioral Verilog Code
Structural Verilog
module MUX (f, a, b, sel);
output f;
input a, b, sel;
and #5 g1 (f1, a, nsel),
g2 (f2, b, sel);
or #5 g3 (f, f1, f2);
not g4 (nsel, sel);
endmodule
a
b
f
sel
f =
a • sel’ + b • sel
a
b
f
sel
nsel
f2
f1
module MUX
(f, sel, b, c);
output reg f;
input sel, b, c;
always @ (sel or b or c)
begin
if (sel == 1)
f = b;
else
f = c;
end
endmodule
Behavioral Verilog
Adapted from Slides of Prof. Don Thomas, CMU

## Slide 38: Structural Verilog: 4:1 Mux

## Slide 39: Behavioral Verilog

## Slide 40: Verilog: 4-to-1 mux via cascaded ternary operator
module mux4to1 (w0, w1, w2, w3, S, f);
input w0, w1, w2, w3;
input [1:0] S;
output f;
assign f = S[1] ? (S[0] ? w3 : w2) : (S[0] ? w1 : w0);
endmodule

## Slide 41: Verilog: 2-to-1 mux via “if-else”
module mux2to1 (w0, w1, s, f);
input w0, w1, s;
output reg f;
always @(w0, w1, s)
if (s==0)
f = w0;
else
f = w1;
endmodule

## Slide 42: Verilog: 4-to-1 mux via case statement
module mux4to1 (W, S, f);
input [3:0] W;
input [1:0] S;
output reg f;
always @(W, S)
case (S)
0: f = W[0];
1: f = W[1];
2: f = W[2];
3: f = W[3];
endcase
endmodule

## Slide 43: Sensitivity Lists
Explicit Sensitivity List
module circuit
(
//Input Port Definitions
input a,
input b,
input c,
//Output Port Definitions
output reg x,
output reg y,
output reg z
);
// Module Body
always @ (a, b, c)
begin
x = a | b | c;
y = a & b & c;
z = ~(a & b & c);
end
endmodule
Implicit Sensitivity List Using @(*)
module circuit
(
//Input Port Definitions
input a,
input b,
input c,
//Output Port Definitions
output reg x,
output reg y,
output reg z
);
// Module Body
always @ (*)
begin
x = a | b | c;
y = a & b & c;
z = ~(a & b & c);
end
endmodule

## Slide 44: Edge Triggering
A Verilog signal can take on the following values
  0
  1
  X (unknown)
  Z (high-impedance)
An edge is a signal transition
  A NEGEDGE is on the transitions
    1 -> x, 1 -> z, 1 -> 0
    x -> 0, z -> 0
  A POSEDGE is on the transitions
    0 -> x, 0 -> z, 0 -> 1
    x -> 1, z -> 1
Used to describe “clocked” (synchronous) logic
D
Q
clk
D Flip Flop

## Slide 45: D Flip-Flop Positive Clock Edge Triggered
// Module Body
always @ (posedge clk)
begin
Q <= D;
end
D
Q
clk
D Flip Flop

## Slide 46: D Flip-Flop Negative Clock Edge Triggered
// Module Body
always @ (negedge clk)
begin
Q <= D;
end
D
Q
clk
D Flip Flop

## Slide 47: D Flip-Flop Positive Clock Edge Triggered, Asynchronous Active High Reset
// Module Body
always @ (posedge clk, posedge reset)
begin
//Was it clk or reset that got us here?
if (reset == 1’b1)
begin
Q <= 1’b0;
end
else
begin
Q <= D;
end
end
D
Q
clk
D Flip Flop
reset

## Slide 48: D Flip-Flop Positive Clock Edge Triggered, Asynchronous Active Low Reset
// Module Body
always @ (posedge clk, negedge reset)
begin
if (reset == 1’b0)
begin
Q <= 1’b0;
end
else
begin
Q <= D;
end
end
D
Q
clk
D Flip Flop
reset

## Slide 49: D Flip-Flop Positive Clock Edge Triggered, Synchronous Active High Reset
// Module Body
always @ (posedge clk)
begin
if (reset == 1’b1)
begin
Q <= 1’b0;
end
else
begin
Q <= D;
end
end
D
Q
clk
D Flip Flop
0
D
reset
1
0

## Slide 50: What is Procedural Code?
Code of the type
is referred to as Procedural Code because the statements between the begin and the end are executed procedurally, or in order.
The Block is executed when triggered by a change in any signal in the sensitivity list
  Then the statements in the body of the always block are executed once
always @ (input1 or input2 or …)
begin
if-then-else or case statement
end

## Slide 51: Procedural Block Examples
reg Q;
always @ (W or E or D)
begin
if (E == 1)
begin
Q = D;
end
else
Q = W;
end
end
Q
2-to-1 Mux
D
W
E
1
0
Here ‘Q’ will be updated if any of ‘W’ or ‘E’ or ‘D’ change

## Slide 52: Procedural Block Examples
reg Q;
always @ (E or D)
begin
if (E == 1)
begin
Q = D;
end
end
Whats the value of ‘Q’ when ‘D’ changes but ‘E’ is 0?
D
Q
E
Transparent
Latch
Incomplete conditional assignments are a common bug.
Here ‘Q’ will hold on to its previous value if ‘E’ is 0!!!

## Slide 53: Procedural Block Examples
reg Q;
always @ (E or D)
begin
if (E == 1)
begin
Q = Y;
end
else
begin
Q = D;
end
end
Whats the value of ‘Q’ when ‘Y’ changes?
Incomplete sensitivity lists is a common bug in designs.
Here ‘Q’ will not follow the value of ‘Y’!!!

## Slide 54: Procedural Assignments
Used within behavioral blocks (initial, always)
Two types of assignments
  = //Blocking Assignment
  <= //Non-Blocking Assignment
Can be used to assign to verilog variable types
  reg
  integer
  real

## Slide 55: Blocking Assignments
Blocking Assignments: Uses the “=“ assignment operator
Blocking Assignments: Are evaluated sequentially
Blocking Assignments: Used to describe combinatorial logic

## Slide 56: Non-Blocking Assignments
Non-Blocking Assignments: Uses the <= assignment operator
Non-Blocking Assignments: Are updated simultaneously
Non-Blocking Assignments: Used to describe sequential logic

## Slide 57: Non-Blocking Rules
Execution of Non-Blocking assigments can be thought of as a two-step process:
Evaluate the RHS of all Non-Blocking statements at the beginning of the time step.
Update the LHS of all Non-Blocking statements at the end of the time step.

## Slide 58: Blocking Rules
Execution of Blocking assignments can be viewed as a one-step process:
Evaluate the RHS and update the LHS of the blocking assignment without interrupt from any other Verilog statement

## Slide 59: Implement this in Verilog
D
Q
clk
D Flip Flop
D
Q
clk
D Flip Flop
D
Q
clk
D Flip Flop
q1
q2
q3
d
clk

## Slide 60: Design 1
Q1: Does this work?
Q2: Is this good Verilog style?
module pipe
(
input [7:0] d,
input clk,
output reg [7:0] q3
);
reg [7:0] q2, q1;
always @ (posedge clk)
begin
q1 = d;
q2 = q1;
q3 = q2;
end
endmodule
Q1: NO (what does this actually become?) Q2: NO (see Q1 above)
(Blocking vs. Non-Blocking: Brown & Vranesic Section 5.12.3)

## Slide 61: Design 2
Q1: Does this work?
Q2: Is this good Verilog style?
module pipe
(
input [7:0] d,
input clk,
output reg [7:0] q3
);
reg [7:0] q2, q1;
always @ (posedge clk)
begin
q3 = q2;
q2 = q1;
q1 = d;
end
endmodule
Q1: Yes (Why does this work when design one does not?) Q2: Not really – it works, but you shouldn’t have to be this careful with the ordering
(Blocking vs. Non-Blocking: Brown & Vranesic Section 5.12.3)

## Slide 62: Design 3
Q1: Does this work?
Q2: Is this good Verilog style?
module pipe
(
input [7:0] d,
input clk,
output reg [7:0] q3
);
reg [7:0] q2, q1;
always @ (posedge clk)
q1 = d;
always @ (posedge clk)
q2 = q1;
always @ (posedge clk)
q3 = q2;
endmodule
Q1: Unknown! (Order of evaluation is undefined. Could work like Design 2 or fail like Design 1 or fail differently than Design 1.) Q2: NO (see Q1 above)
(Blocking vs. Non-Blocking: Brown & Vranesic Section 5.12.3)

## Slide 63: Design 4 (Non-Blocking)
module pipe
(
input [7:0] d,
input clk,
output reg [7:0] q3
);
reg [7:0] q2, q1;
always @ (posedge clk)
begin
q1 <= d;
q2 <= q1;
q3 <= q2;
end
endmodule
module pipe
(
input [7:0] d,
input clk,
output reg [7:0] q3
);
reg [7:0] q2, q1;
always @ (posedge clk)
begin
q3 <= q2;
q2 <= q1;
q1 <= d;
end
endmodule
Works? YES! Good style? YES!
(Blocking vs. Non-Blocking: Brown & Vranesic Section 5.12.3)

## Slide 64
Figure 6.4. State table for the sequential circuit in Figure 6.3.
Present
Next state
Output
state
w
=
0
w
=
1
z
A
A
B
0
B
A
C
0
C
A
C
1

## Slide 65
Figure 6.29. Verilog code for the FSM in Figure 6.3.
module simple (Clock, Resetn, w, z);
input Clock, Resetn, w;
output z;
reg [2:1] y, Y;
parameter [2:1] A = 2'b00, B = 2'b01, C = 2'b10;
// Define the next state combinational circuit
always @(w, y)
case (y)
A: if (w) Y = B;
else Y = A;
B: if (w) Y = C;
else Y = A;
C: if (w) Y = C;
else Y = A;
default: Y = 2'bxx;
endcase
// Define the sequential block
always @(negedge Resetn, posedge Clock)
if (Resetn = = 0) y <= A;
else y <= Y;
// Define output
assign z = (y = = C);
endmodule

## Slide 66
Figure 6.33. Second version of code for the FSM in Figure 6.3.
module simple (Clock, Resetn, w, z);
input Clock, Resetn, w;
output reg z;
reg [2:1] y, Y;
parameter [2:1] A = 2'b00, B = 2'b01, C = 2'b10;
// Define the next state combinational circuit
always @(w, y)
begin
case (y)
A: if (w) Y = B;
else Y = A;
B: if (w) Y = C;
else Y = A;
C: if (w) Y = C;
else Y = A;
default: Y = 2'bxx;
endcase
z = (y = = C); //Define output
end
// Define the sequential block
always @(negedge Resetn, posedge Clock)
if (Resetn = = 0) y <= A;
else y <= Y;
endmodule

## Slide 67
Figure 6.34. Third version of code for the FSM in Figure 6.3.
module simple (Clock, Resetn, w, z);
input Clock, Resetn, w;
output z;
reg [2:1] y;
parameter [2:1] A = 2'b00, B = 2'b01, C = 2'b10;
// Define the sequential block
always @(negedge Resetn, posedge Clock)
if (Resetn = = 0) y <= A;
else
case (y)
A: if (w) y <= B;
else y <= A;
B: if (w) y <= C;
else y <= A;
C: if (w) y <= C;
else y <= A;
default: y <= 2'bxx;
endcase
// Define output
assign z = (y = = C);
endmodule

## Slide 68: Figure 6.35. Verilog code for the FSM in Figure 6.11.
module control (Clock, Resetn, w, R1in, R1out, R2in, R2out, R3in, R3out,Done);
input Clock, Resetn, w;
output R1in, R1out, R2in, R2out, R3in, R3out, Done;
reg [2:1] y, Y;
parameter [2:1] A = 2'b00, B = 2'b01, C = 2'b10, D = 2'b11;
// Define the next state combinational circuit
always @(w, y)
case (y)
A: if (w) Y = B;
else Y = A;
B: Y = C;
C: Y = D;
D: Y = A;
endcase
// Define the sequential block
always @(negedge Resetn, posedge Clock)
if (Resetn = = 0) y <= A;
else y <= Y;
// Define outputs
assign R2out = (y = = B);
assign R3in = (y = = B);
assign R1out = (y = = C);
assign R2in = (y = = C);
assign R3out = (y = = D);
assign R1in = (y = = D);
assign Done = (y = = D);
endmodule

## Slide 69: Figure 6.36. Verilog code for the Mealy machine of Figure 6.23.
module mealy (Clock, Resetn, w, z);
input Clock, Resetn, w;
output reg z;
reg y, Y;
parameter A = 1’b0, B = 1’b1;
// Define the sequential block
always @(negedge Resetn, posedge Clock)
if (Resetn = = 0) y <= A;
else y <= Y;
// Define the next state and output combinational circuits
always @(w, y)
case (y)
A: if (w)
begin
z = 0;
Y = B;
end
else
begin
z = 0;
Y = A;
end
B: if (w)
begin
z = 1;
Y = B;
end
else
begin
z = 0;
Y = A;
end
endcase
endmodule